# This assignments is in order of your notes! You may work with a partner.

- What is the difference between Static electricity and Current electricity?

- Complete the chart below

|  | Definition | 2 examples |
| --- | --- | --- |
| Insulator |  |  |
| Conductor |  |  |

3. Complete this chart for parts of the circuit

|  | Function | Proper Electrical Symbol |
| --- | --- | --- |
| Battery |  |  |
| Switch |  | Open: Closed: |
| Light bulb | Converts electrical energy to ________ and ________ energy. |  |
| Wires |  |  |

4. Name 2 other loads and the type of energy that the electrical energy gets converted to.

|  | Converts electrical energy to |
| --- | --- |
|  | Converts electrical energy to ________ and ________ energy. |

5. Complete the Chart

|  | Definition | Symbol | Device to measure it | Units |
| --- | --- | --- | --- | --- |
| Voltage |  |  |  |  |
| Current |  |  |  |  |
| Resistance |  |  | Can be calculated or Use ohmmeter |  |

- What is happening inside the battery that produces energy for the electrons?

- Electrons flow from the ________________ terminal of a battery to the ___________________ terminal.

- a. Calculate the voltage drop of a food blender that has a resistance of 65 ohms and a current of 1.85 A flowing through it.

- A current of 12 A flows through a red-hot stove element when the voltage drops across the element is 240 V.  Calculate the resistance of the element.

- Draw a circuit with 3 cells connected in series, having a load, switch, resistor and ammeter.

- In order to measure current, is the ammeter connected in series or in parallel with the other parts of the circuit?  __________________

- What happens to current when you increase the resistance in your circuit? _________

- What type of circuit do you create when a battery is connected directly to itself (no load)? __________________ _______________ . Why is this dangerous?

- Complete the chart below for cells connected in series and in parallel

|  | Cells (batteries) in Series | Cells in Parallel |
| --- | --- | --- |
| Explain how the cells are connected |  |  |
| State the trend in voltage (increase/decrease or stay the same) |  |  |

- If 10 cells each having a voltage of 1.5 are connected in series what would be the total electric potential of the electrons?

________________

- If 10 cells each have a voltage of 1.5 and are connected in parallel what would be the total voltage?

_________________

- What is the purpose of connecting cells (batteries)  in parallel?

- Draw a circuit with 2 cells connected in parallel, hooked up to a voltmeter, 2 light bulbs connected in parallel, open switch and an ammeter. Be careful how the voltmeter and the ammeter are connected.

- Complete the chart for connecting loads (i.e. light bulbs) in parallel and series.

|  | Series | Parallel |
| --- | --- | --- |
| Current |  |  |
| Resistance |  |  |
| Effect of unscrewing one bulb |  |  |
| Brightness of the bulb |  |  |

- Why are the circuits in a home wired in parallel?

- a) If a machine takes in 50 J (Joules) of electrical energy and puts out 45 J what is its efficiency of the machine?

b) What happened to the other 5 Joules of energy?

21. Match up the following Alternative Energies

# Text boxes

Current Electricity Assignment

Name:

Date: